## Slide 1: Development of Model-data Assimilation framework
Tyler Hesser, PhD
Matthew Farthing, PhD
Coastal and Hydraulics Laboratory
US Army Engineer R&D Center
22 June 2017

## Slide 2: UAS support to frm
GOAL: “To identify and develop defendable and consistent Unmanned Aerial System (UAS)-based methodology and data products that seamlessly integrate with numerical models to monitor topography and bathymetry, storm-damage reduction infrastructure, and ecosystem health to improve USACE’s management of flood risks.”
Multi-Lab initiative (CHL/GRL/EL/CRREL)
Funded by: Flood & Coastal, CODS, CFDC

## Slide 3
Neashore Data Assimilation Framework
PI – Tyler Hesser
Combine UAS data sources using data assimilation framework
Use novel and well tested black-box data assimilation schemes to combine:
  Beach topography
  Dune shape
  Vegetation growth
  Historical LIDAR bathymetry
  Inverted bathymetry from sea surface measurements
Build short term forecast using USACE tools for flood risk
- Use data assimilation to build an accurate forward prediction model for flood risk.
Capabilities/Applications
Data assimilation framework to combine data from multiple UAS platforms
Couple data assimilation tools with existing USACE flood risk numerical prediction models
Super-storm Sandy led to wide spread beach erosion from Virginia to New York.
UAS observations provide pre-storm conditions
Data assimilation framework provides an estimate of pre-storm conditions

## Slide 4: What is the role of data assimilation with uas technology?
UAS technology provides a unique observation of the environment at a single time.
Lack of continuous observation reduce the accuracy of the inversion analysis
Higher fidelity physics can pull more out of observation data sets and improve prediction between observations

## Slide 5: What is the role of data assimilation for Hurricane Flood Risk?
Background Bathymetry
JALBTCX (1-2 yrs)
UAS Hurricane Season
Model Risk Assessment
Hurricane Forecast
Pre-Storm UAS
Data Assimilation coupled to CSTORM for flood risk prediction
Hurricane
Post Storm Assessment

## Slide 6: What is data assimilation for nearshore processes?
Estimate depths and other material properties for mobility in the nearshore
Combine direct estimation from measurements with data assimilation

## Slide 7: Surface Signature of Waves
Linear
Dispersion Eqn:
As waves enter shallow water, they slow down.
By measuring these changes in speed, we can use physics equations to determine the water depth.

## Slide 8: Surface Signature of Waves
As waves break energy is dissipated
Requires estimates of wave breaking dissipation from model to relate to depth
Dissipation
Energy loss from breaking over bar
Energy loss from breaking at the shore

## Slide 9: Difficulty with Inversion?
Open Coast
Open Coast with rip currents
Inlet dynamics
Physical Complexity
Inversion Difficulty

## Slide 10: Nearshore Model Based Inversion
Observations
Numerical Modeling Framework
Data Assimilation Module
Improved Bathymetry
Boundary Forcing

## Slide 11: Use of measurements for data assimilation
Wave speed
Topography
Breaking Dissipation

## Slide 12: Nearshore Model Based Inversion
Observations
Numerical Modeling Framework
Data Assimilation Module
Improved Bathymetry
Boundary Forcing

## Slide 13: Nearshore Model Framework
Computation Time
Model Fidelity
Linear Theory
Phase Averaged Model
Coupled Wave-Circulation
Phase Resolving Models

## Slide 14: Nearshore Model Based Inversion
Observations
Numerical Modeling Framework
Data Assimilation Module
Improved Bathymetry
Boundary Forcing

## Slide 15: Data Assimilation
Data assimilation uses relationships between modeled and observed quantities to improve forecasts and predictions through measured data.
Collaborations with:
- Stanford University
- NC State University
- Oregon State University
to develop efficient and accurate data assimilation methods

## Slide 16: What is the role of data assimilation for Hurricane Flood Risk?
Background Bathymetry
JALBTCX (1-2 yrs)
UAS Hurricane Season
Model Risk Assessment
Hurricane Forecast
Pre-Storm UAS
Data Assimilation coupled to CSTORM for flood risk prediction
Hurricane
Post Storm Assessment

## Slide 17: How does data assimilation from Uas for Flood Risk work?
Initial Bathymetry
6 months prior
UAS Assimilated Bathymetry

## Slide 18: How does data assimilation from Uas for Flood Risk work?
Initial Bathymetry
6 months prior
UAS Assimilated Bathymetry

## Slide 19: Data assimilation UAS Example
Inverted bathymetry
Wave speeds
Profile result
P1
P2
P1
P2

## Slide 20: Nearshore Model Based Inversion
Observations
Numerical Modeling Framework
Data Assimilation Module
Improved Bathymetry
Boundary Forcing
RIVERINE

## Slide 21: Riverine Assessment
Estimate bathymetry by optimizing the comparison of flow simulations in channels to observed surface currents
Novel inversion techniques that are robust for “snapshot” data
Observed surface currents
Savannah River, GA
Updated high
resolution estimates
of channel bathymetry
and flow conditions
Bathymetry Estimates and Uncertainty
Ensemble Kalman Filter
PCGA

## Slide 22: Future Work
Include higher fidelity models and morphology estimation
Include vegetation assessment from UAS into flood risk prediction
Improve assimilation in inlet dynamics and flood risk from back bay inundation.
Robustness over longer assimilation windows
Improved estimation of uncertainty

## Slide 23: Could we use this technology to monitor nearshore morphology Evolution?
Background Bathymetry
JALBTCX (1-2 yrs)
UAS surveys
~ 1 month
Data Assimilation for improved monitoring of morphology
Post Placement Assessment
Beach nourishment
Use numerical modeling to monitor environment (c2shore for morphology)
Post placement survey

## Slide 24: Questions?